2002 Written Dive Plan Assessment Answers

- Assuming fine weather, what will be the general tidal conditions that day?

Answer:

Strong currents due to Spring Tides (High Springs)		10 marks

- What would be the most suitable time on the Wednesday to have the divers enter the water to survey and photograph the wreck? State your reason(s)?

Answer:

Tidal Diamond ‘D’ indicates LW slack is 5hrs after HW Plymouth. Low water slack is best due to least current and shallowest water. HW is 07:08BST therefore slack will be slightly before 12:08hrs. This will allow time for a second dive later in the day.

10 marks

- What arrangements would you make regarding the “Dry Cox” and why?

Answer:

Arrange to have an experienced Cox in each boat. This is a new location with significant currents and a potentially deep and long dive. There is also the possibility of commercial shipping in the area.

10 marks

- What is your prediction/estimation of the tidal current rate and direction during the dive?

Answer:

At 12:08hrs the current should be approx. 0.5 knots with a direction of 125o True.

10 marks

- What time would your RIB’s leave the marina in Dartmouth to head to the dive-site? What factors would you allow for?

Answer:

Distance is 7 NM @ 10 kts	= 45 minutes (reduced speed in to harbour)

Await slack/find wreck	= 20 mins

Kitup				= 10 mins

Time in hand			= 15 mins

Total	= 90 mins

Depart 10:30 hrs latest

(Realistic estimate, within +/- 15 minutes)				10 marks

- What ETR would you give the Shore-marshall? What factors would you allow for?

Answer:

Assume Dry Cox’n and one stick diving

Travel out			= 90 mins (above)

Group in water		= 60 mins

Return time			= 45 mins

Time in hand			= 60 mins

Total				   4.25 hrs

Depart 10:30 + 4.25 hrs = 14:45 approx

(Realistic estimate within +/- 20 minutes)				10 marks

- One of your group informs you that they have not undertaken a wreck dive before. What would you advise them about? What precautions would you take to improve safety?

Answer:

Monitor, depth, time, air & buddy carefully

Problems with using compass near steel hull, dis-orientation

Danger of nets, sharp edges, overhangs and overhead obstacles

Risks when entering wrecks

Possible loss of visibility

Need for extra equipment, torches, safety lines etc

( 2marks for each suitable answer)		10 marks

- List what information you would get from each diver at the brief prior to this dive.

Answer:

Bottle Capacity & pressure

Previous/recent dive experience, dived up, qualified, experienced

RNT

Computer or tables

Any problems/issues

Any particular personal dive plan, camerawork surveys

( 2marks for each suitable answer)		10 marks

- List five (5) safety points specific to this dive that you will include in your brief.

Answer:

Buddy & signals checks

Separation/drifting procedures

Deep dive, NDL, safety stops

Use of SMB’s

Detail of conditions expected

Details layout, position of site/wreck

Position of shotline

( 2marks for each suitable answer)		10 marks

- Outline five (5) important pieces of information you would seek as part of your ‘Advance’ and ‘Pre-dive’ planning for this week diving.

Answer:

Weather forecasts

Access to water and moorings

Tidal anomalies

Local conditions/advice

Necessary permission required e.g war wrecks

Availability of air/fuel

( 2marks for each suitable answer)		10 marks